## Slide 1: x86 Intel Architecture
Instructor: john ortiz
Lecturer III utsa
stego@satx.rr.com
CS 3843 computer organization

## Slide 2: Basic Execution Environment
How the processor executes instructions and manipulates data
Memory Model
Address Space
General Purpose Data Registers
Segment Registers
Flags Register
Instruction Pointer

## Slide 3: Basic Execution Environment
3 Modes of Operation for IA-32 Architecture
  Protected Mode
  Real-Address Mode
  System Management Mode
Each Operating Mode determines which instructions and architectural features are accessible

## Slide 4: Basic Execution Environment

## Slide 5: Memory Models
Address Space
  Linear Address up to 4 GB
  Physical Address Space up to 64 GB
Real Address Mode Memory Model
  Memory model for the Intel 8086
  Uses specific implementation of segmented memory
    Array of segments up to 64 Kbytes each
    Linear address space is 1 MB ( 220 )
Flat Memory Model
  Memory is a single contiguous address space
  Linear Address Range 0 to 232 – 1 (0x0 - 0xFFFFFFFF)

## Slide 6: Memory Models
Segmented Memory Model
  Memory is a group of independent address spaces
  Code, data, stacks are generally in different segments
  Segment selector identifies the segment and an offset identifies the byte within the segment
  16383 segments
    Each up to 232 bytes
Using segments can prevent the stack from growing into code

## Slide 7: Segmented Memory Model
Each segment can point to overlapping (or not) virtual memory

## Slide 8: Memory Models
Implementation on Windows sets most segments to point to the same linear address space
Effectively a flat memory model with a linear address space of 4GB
  ONE EXCEPTION: FS is used to point to different memory for the Process Environment Block

## Slide 9: Paging and Virtual Memory
Physical memory is the hardware, the memory you buy and put into the machine
Virtual memory allows every 32-bit process to seemingly have 4 GB of memory
  Virtual addresses are mapped to physical memory in 4K pages (on a 32-bit system)
  Only physical memory required by a process is actually used
  When more memory is needed than physical memory available, the physical memory can be swapped to disk

## Slide 10: Paging and Virtual Memory
Suppose I have 32K (yes, kilo) bytes of physical memory
How many 4K pages are available?

## Slide 11: Paging and Virtual Memory
Suppose I have 32K (yes, kilo) bytes of physical memory
How many 4K pages are available?
  8 --- > 8 * 4K = 32K
Suppose I have 16 address lines
How many possible addresses can I access?

## Slide 12: Paging and Virtual Memory
Suppose I have 32K (yes, kilo) bytes of physical memory
How many 4K pages are available?
  8 --- > 8 * 4K = 32K
Suppose I have 16 address lines
How many possible addresses can I access?
  65536 == 64K == log2-1(16) == 216

## Slide 13: Paging and Virtual Memory
One processes needs 20K, so it will have 5 pages mapped directly to physical memory
  Not necessarily contiguously
It “thinks” it has a full 64K available
  For our fictitious 16-bit address line
  0x0 to 0xFFFF
So maybe one address used may be 0x0000
  Does NOT have to be mapped to physical address 0x0000!!
Another address may be 0xc000
  0xc000 > 32K (0x7FFFF), but can be mapped to any unused physical address within the 32K range
Mapping is fast, done by hardware & software
  Level 1 and level 2 caches help

## Slide 14: Paging and Virtual Memory
0x0000
0x1000
0x2000
0x3000
0x4000
0x5000
0x6000
0x7000
Process #1: 0x0000
Process #1: 0x1000
Process #1: 0x7000
Process #1: 0xc000
Process #1: 0xf000
Process #2: 0x3000
Process #2: 0x4000
Process #2: 0xf000
Virtual Memory
Physical Memory
If a third process needs some memory, then a page (or more) will be saved to disk, (in the paging file) and that process will get the physical RAM for its time slot

## Slide 15: Paging and Virtual Memory
For the programmer, every 32-bit process “thinks” it has a full 4 GB of address space
  Regardless of physical RAM availability
  Regardless of physical RAM address
One process cannot simply access the memory of another process
  0x10000 on one process is mapped to different physical RAM than 0x10000 in another process
Must use Interprocess communication

## Slide 16: Paging and Virtual Memory
How many 4k pages in 32 bits?
  You should be able to do this quickly on paper

## Slide 17: Paging and Virtual Memory
How many 4k pages in 32 bits?
  You should be able to do this quickly on paper
  4K = 212
  232 / 212 = 220 = 1 M = 0x 100000 = 1048576

## Slide 18: Memory Classifications
Applies to both Windows and Linux though actual addresses will be different
Kernel Memory
  Reserved for kernel usage
Program Memory
  Includes code and data
    Constant values such as strings
    Multimedia
    Debugging tables
    Global/static variables
Heap Memory
Stack Memory
Unassigned

## Slide 19: Registers
Eight general purpose registers ( 32 bits )
  eax, ebx, ecx, edx, esi, edi, ebp, esp
Six segment registers ( 16 bits )
  cs, ds, ss, es, fs, gs
One flags register
  eflags
  Reports the status of the program being executed and allowed limited control of the processor
One Instruction Pointer
  eip
  Points to next instruction to be executed
*Note: “e” stands for extended (i.e. 32 bits)
  “eax” is extended ax register

## Slide 20: Registers
No 8-bit versions

## Slide 21: General Purpose Registers
EAX - Extended Accumulator
  Accumulator for operands and results data
EBX - Extended Base register
  Pointer to data in the DS segment
ECX - Extended Count register
  Counter for string and loop operations
EDX - Extended Data register
  I/O Pointer, general data

## Slide 22: General Purpose Registers
ESI - Extended Source Index
  Pointer to data in the DS segment
  Source pointer for string operations
EDI - Extended Destination Index
  Pointer to data in the DS segment
  Destination pointer for string operations
ESP - Extended Stack Pointer
  Stack pointer (in the stack segment)
EBP - Extended Base Pointer
  Pointer to data on the stack (in the stack segment)

## Slide 23: Segment Registers
CS - Code Segment
  Pointer to executable code
  eip is the offset into the code segment
SS - Stack Segment
  Pointer to the stack
  stack pointer is the offset in the stack segment
DS - Data Segment
  Pointer to data in the DS segment
ES - Extra Segments for data
FS - Extra Segment for data (386 and above)
GS - Extra Segment for data (386 and above)

## Slide 24: Segment Registers
In Windows, except for FS, all segment registers point to the same place in memory
  Linux also uses a flat memory model and paging
Also, it is possible to do a segment override on a per instruction basis
  Tell a particular instruction to use a different segment

## Slide 25: Instruction Pointer
EIP points to the next machine code instruction to be executed
x86 is a CISC architecture
  Complex instruction set
    Many instructions, different sizes
  RISC is Reduced Instruction Set
Automatically incremented when each instruction is executed
  The amount incremented depends on the instruction and its arguments

## Slide 26: Instruction Pointer
Cannot be accessed directly by software
  There is no “mov eip, eax” type of instruction
  Can be “loaded” by jump, call, and branch instructions
  Could load eip as follows:
    push eax
    return
  But can also call eax – so why do the above???

## Slide 27: Instruction Pointer
Cannot be accessed directly by software
  There is no “mov eip, eax” type of instruction
  Can be “loaded” by jump, call, and branch instructions
  Could load eip as follows:
    push eax
    return
  But can also call eax – so why do the above???
    Malware takes advantage of that!
  Can be read as follows:
    call label
    label: pop eax
    ; eax now has the address of label
  eip is incremented immediately after reading the instruction
    We’ll see why that is important later

## Slide 28: Flags Register
EFLAGS keeps status flags, control flags, and system flags

## Slide 29: Flags Register
NOTE: for ALL Flag Register examples, using 8 bits
CF – Carry Flag
  Set if arithmetic operation generates a carry or borrow out of the MSB, cleared otherwise
    MSB might be bit 7, bit 15, bit 31 depending on operation size
  It is overflow for unsigned arithmetic
    0xFF + 1 = 0x100 --- sets carry
    0x05 – 0x06 = 0xFF --- also sets carry (i.e. generates borrow)
      0 0000 0101 + 1 1111 1010 = 1 1111 1111
    0x05 – 0x04 = 0x01 does NOT set carry
      0 0000 0101 + 1 1111 1100 = 0 0000 0001
  All logical operations clear the carry flag
ZF – Zero Flag
  Set if result of operation is zero, cleared otherwise
  Set by add/sub and logical operations

## Slide 30: Flags Register
SF – Sign Flag
  Set equal to the MSB of the result
    MSB may be at bit 7, 15, or 31 depending on size of operation
  1 indicates a negative result
  0111 1111 + 1 = 1000 0000 --- > sign flag is set
  If result is 128 to 255, sign flag set (8 bits ONLY)
OF – Overflow Flag
  Set if the result overflows into the sign bit
    Too large of a positive number
    Too small of a negative number
    Overflow for signed arithmetic
  Set when
    Two positive operands generate a negative sum
    Two negative operands generate a positive sum

## Slide 31: Flags Register
char x = 0x7f; (x = 127)
  Largest possible positive number for 8 bits
x = x + 1; now x == 0x80 (128)
  0x80 is -128 in signed arithmetic: 127 + 1 = -128???
  OF flag is set to indicate the overflow
  127 + 1 OR -128 – 1 [-128 + -1] set overflow
Overflow always cleared if two addends have different signs
Compiler will set the assembly code to act on it if it’s a signed value
  Unsigned branch instructions do NOT act on it
  Signed branch instructions take its value into account

## Slide 32: Flags Register
PF – Parity Flag
  Set if least significant byte of the result has an even number of bits, cleared otherwise
AF – Auxiliary Carry Flag
  Set if operation generates a carry out of bit 3, cleared otherwise
  Used for Binary Coded Decimal (BCD) arithmetic
    In BCD, 9 + 1 = 0, carry the 1
    Each nibble has one decimal digit, 0 to 9
    So 38 + 1 = 39 --- > 0011 1000 + 1 = 0011 1001
    39 + 1 = 40 --- > 0011 1001 + 1 = 0100 0000, NOT 0011 1010

## Slide 33: Flags Register
DF – Direction Flag
  Applies to string instructions only
    movs, cmps, scas, lods, stos
  Determines if esi/edi are incremented or decremented
    Size of operation determines amount: 1, 2, or 4
TF – Trap Flag
  Used for single-stepping the processor
  Windbg makes use of this flag
IF – Interrupt Enable Flag
  Enables/disables interrupts
IOPL – I/O Privilege Level
  Prevents users from executing privileged instructions
Rest of the flags, you can read about on your own

## Slide 34: Endian
Big Endian
  Motorola based products use Big Endian
  MSB (most significant byte) is in lowest memory address
  Easy to read when looking at memory
  0x400000: 01 23 45 67
    Value = 0x1234567
Little Endian
  Intel products use little endian
  MSB is in highest address
  0x400000: 01 23 45 67
    Value is 0x67452301

## Slide 35: Alignment
Generally data is aligned to its inherent size
DWORD (32 bits, 4 bytes) is aligned to a 4-byte boundary
  0x0000, 0x0004, 0x0008, etc
WORD (16 bits, 2 bytes) is aligned to a 2-byte boundary
  0x0000, 0x0002, 0x0004, etc
In binary, a 2-byte boundary will always end in 102, i.e. least significant bit is zero
A 4-byte boundary in 1002, i.e. least significant 2 bits are zero
Misaligned data is less efficient, but possible

## Slide 36: The Stack
The stack is memory set aside to be used as temporary storage during function calls
Typically, it’s used for …
  1. ???
  2. ???
  3. ???
  4. ???
  5. ???

## Slide 37: The Stack
The stack is memory set aside to be used as temporary storage during function calls
Typically, it’s used for …
  1. Local Variables
    char x; int y; etc.
  2. ???
  3. ???
  4. ???
  5. ???

## Slide 38: The Stack
The stack is memory set aside to be used as temporary storage during function calls
Typically, it’s used for …
  1. Local Variables
    char x; int y; etc.
  2. Function parameters
    Func (param 1, param 2, param 3 … )
    The parameters are pushed onto the stack in reverse order
      param #3, param #2, param #1
  3. ???
  4. ???
  5. ???

## Slide 39: The Stack
The stack is memory set aside to be used as temporary storage during function calls
Typically, it’s used for …
  1. Local Variables
    char x; int y; etc.
  2. Function parameters
    Func (param 1, param 2, param 3 … )
    The parameters are pushed onto the stack in reverse order
      param #3, param #2, param #1
  3. Return Address
    When a function is called, the address of the next instruction is pushed onto the stack after the parameters
  4. ???
  5. ???

## Slide 40: The Stack
The stack is memory set aside to be used as temporary storage during function calls
Typically, it’s used for …
  1. Local Variables
    char x; int y; etc.
  2. Function parameters
    Func (param 1, param 2, param 3 … )
    The parameters are pushed onto the stack in reverse order
      param #3, param #2, param #1
  3. Return Address
    When a function is called, the address of the next instruction is pushed onto the stack after the parameters
  4. EBP – this is often pushed onto the stack during a function call to set up the stack frame
  5. ???

## Slide 41: The Stack
The stack is memory set aside to be used as temporary storage during function calls
Typically, it’s used for …
  1. Local Variables
    char x; int y; etc.
  2. Function parameters
    Func (param 1, param 2, param 3 … )
    The parameters are pushed onto the stack in reverse order
      param #3, param #2, param #1
  3. Return Address
    When a function is called, the address of the next instruction is pushed onto the stack after the parameters
  4. EBP – this is often pushed onto the stack during a function call to set up the stack frame
  5. Temp storage for registers

## Slide 42: Stack Operations
The following instructions are used in conjunction with stack operations
  push register
  pop register
  call function
  retn
Anyone want to explain any of these
  BEFORE looking to the next slide :/

## Slide 43: Questions & Comments

## Slide 44: References
https://msdn.microsoft.com/en-us/library/windows/desktop/aa365574(v=vs.85).aspx
Intel Reference Manuals
https://en.wikipedia.org/wiki/X86_memory_segmentation