## Slide 1: x86 Intel Architecture
Instructor: john ortiz
Lecturer III utsa
stego@satx.rr.com
CS 3843 computer organization

## Slide 2: Memory Classifications
Applies to both Windows and Linux though actual addresses will be different
Kernel Memory
  Reserved for kernel usage
Program Memory
  Includes code and data
    Constant values such as strings
    Multimedia
    Debugging tables
    Global/static variables
Heap Memory
Stack Memory
Unassigned

## Slide 3: Endian
Big Endian
  Motorola based products use Big Endian
  MSB (most significant byte) is in lowest memory address
  Easy to read when looking at memory
  0x400000: 01 23 45 67
    Value = 0x1234567
Little Endian
  Intel products use little endian
  MSB is in highest address
  0x400000: 01 23 45 67
    Value is 0x67452301

## Slide 4: The Stack
The stack is memory set aside to be used as temporary storage during function calls
Typically, it’s used for …
  1. ???
  2. ???
  3. ???
  4. ???
  5. ???

## Slide 5: The Stack
The stack is memory set aside to be used as temporary storage during function calls
Typically, it’s used for …
  1. Local Variables
    char x; int y; etc.
  2. ???
  3. ???
  4. ???
  5. ???

## Slide 6: The Stack
The stack is memory set aside to be used as temporary storage during function calls
Typically, it’s used for …
  1. Local Variables
    char x; int y; etc.
  2. Function parameters
    Func (param 1, param 2, param 3 … )
    The parameters are pushed onto the stack in reverse order
      param #3, param #2, param #1
  3. ???
  4. ???
  5. ???

## Slide 7: The Stack
The stack is memory set aside to be used as temporary storage during function calls
Typically, it’s used for …
  1. Local Variables
    char x; int y; etc.
  2. Function parameters
    Func (param 1, param 2, param 3 … )
    The parameters are pushed onto the stack in reverse order
      param #3, param #2, param #1
  3. Return Address
    When a function is called, the address of the next instruction is pushed onto the stack after the parameters
  4. ???
  5. ???

## Slide 8: The Stack
The stack is memory set aside to be used as temporary storage during function calls
Typically, it’s used for …
  1. Local Variables
    char x; int y; etc.
  2. Function parameters
    Func (param 1, param 2, param 3 … )
    The parameters are pushed onto the stack in reverse order
      param #3, param #2, param #1
  3. Return Address
    When a function is called, the address of the next instruction is pushed onto the stack after the parameters
  4. EBP – this is often pushed onto the stack during a function call to set up the stack frame
  5. ???

## Slide 9: The Stack
The stack is memory set aside to be used as temporary storage during function calls
Typically, it’s used for …
  1. Local Variables
    char x; int y; etc.
  2. Function parameters
    Func (param 1, param 2, param 3 … )
    The parameters are pushed onto the stack in reverse order
      param #3, param #2, param #1
  3. Return Address
    When a function is called, the address of the next instruction is pushed onto the stack after the parameters
  4. EBP – this is often pushed onto the stack during a function call to set up the stack frame
  5. Temp storage for registers

## Slide 10: Stack Operations
The following instructions are used in conjunction with stack operations
  push register
  pop register
  call function
  retn
Anyone want to explain any of these
  BEFORE looking to the next slide :/

## Slide 11: Stack Operations - PUSH
push eax
  Puts the contents of eax on the stack
  Since esp points to last valid stack value, first it is decremented
    esp = esp -4 ; always on 4-byte boundary
  Then the value in eax is copied to the new location
Example: eax = 0x1234ABCD, esp = 0x12894
  esp = esp – 4 = 0x12890
  memory location 0x12890 gets a new value, 0x1234ABCD
  Stored in little endian format: CD AB 34 12
    0x12890 = 0xCD
    0x12891 = 0xAB
    0x12892 = 0x34
    0x12893 = 0x12
eip is incremented after reading the push instruction

## Slide 12: Stack Operations - POP
pop eax
  Puts the contents of the stack into eax
  Since esp points to last valid stack value, first that value is copied to eax
  Then esp is incremented
  esp = esp + 4 ; always on 4-byte boundary
Example: [esp]= 0x1234ABCD, esp = 0x12890
  get value from memory location 0x12890
    [0x12890] = 0xCDAB3412
  eax = 0x1234ABCD
  esp = esp + 4 = 0x12894
eip is incremented after reading the pop instruction

## Slide 13: Stack Operations - CALL
call <function>
Begins execution of <function> and saves return address
  Loads the address of <function> into eip
  Pushes the return address onto the stack
  In this example the address of the function is stored in eax
Example: call eax, esp = 0x12890, eax=0x400100
  assume this call instruction is 2 bytes long
  eip is incremented by 2
  now eip IS the return address
  push eip to the stack
    esp = esp – 4
    [esp] = eip
  Set eip to the function address
  eip = eax = 0x400100

## Slide 14: Stack Operations - RETN
retn
Returns from a function call using the saved address
  Pops the address on the stack into eip
    mov eip,[esp]
    esp = esp + 4
  Begins execution at this address
Example: retn, esp = 0x12890
  eip = [0x12890]
  esp = esp + 4
Note: eip is still incremented after the return instruction, but it’s value is replaced before it begins execution at the next instruction

## Slide 15: The Stack – Function Call
Calling the function “calcNewAge(int,int)”
mov var_240, 0Ah
mov eax, var_240
push eax ; diff = 0x0A, constant
mov ecx, var_228 ;age
push ecx ; var_228 is stack location for age
  For this example, let’s just assume fifty (age = 50 == 0x32)
call j_?calcNewAge@@YAHHH@Z ;mangled name
add esp, 8 ; reset stack pointer

## Slide 16: The Stack – Function Call
int __cdecl calcNewAge(int age, int diff)
  var_CC = byte ptr -0CCh ; IDA Pro labels
  newAge = dword ptr -8 ; constants
  age = dword ptr 8 ; user-entered value
  diff = dword ptr 0Ch
push ebp
mov ebp, esp
sub esp, 0CCh ; reserve space on stack
push ebx
push esi
push edi
  …
mov eax, [ebp+age] ; addr of age is ebp+8
  …
pop edi
pop esi
pop ebx
mov esp, ebp
pop ebp
retn
Labels
{

## Slide 17: The Stack
Prior to function call
in C
calcNewAge(age, diff)
push ==
  decrement ESP
  store value
pop ==
  load value
  increment esp
Address | Value | Instruction
0x1FFCC |  | 
0x1FFD0 |  | 
0x1FFD4 |  | 
0x1FFD8 |  | 
0x1FFDC |  | 
0x1FFE0 |  | 
0x1FFE4 |  | 
0x1FFE8 |  | 
0x1FFEC |  | 
0x1FFF0 |  | 
0x1FFF4 |  | 
0x1FFF8 |  | 
0x1FFFC | value | 
ESP – Top of Stack
EBP=0x12345678

## Slide 18: The Stack
x=calcNewAge(age, diff)
In Assembly Language
0x401000 push diff
0x401001 push age
0x401002 call calcNewAge
0x401007 … next instruction …
Address | Value | Instruction
0x1FFCC |  | 
0x1FFD0 |  | 
0x1FFD4 |  | 
0x1FFD8 |  | 
0x1FFDC |  | 
0x1FFE0 |  | 
0x1FFE4 |  | 
0x1FFE8 |  | 
0x1FFEC |  | 
0x1FFF0 | 07 10 40 00 | call calcNewAge
0x1FFF4 | 32 00 00 00 | push age
0x1FFF8 | 0A 00 00 00 | push diff
0x1FFFC | value | 
ESP
EBP=0x12345678
EIP

## Slide 19: The Stack
Inside function
push ebp
mov ebp, esp
sub esp, 0CCh
Address | Value | Instruction
0x1FFCC |  | 
0x1FFD0 |  | 
0x1FFD4 |  | 
0x1FFD8 |  | 
0x1FFDC |  | 
0x1FFE0 |  | 
0x1FF20 |  | sub esp, 0xcc
--- | … | 
0x1FFEC | 78 56 34 12 | push ebp
0x1FFF0 | 07 10 40 00 | call calcNewAge
0x1FFF4 | 32 00 00 00 | push age
0x1FFF8 | 0A 00 00 00 | push diff
0x1FFFC | value | 
ESP
EBP=0x0001FFEC

## Slide 20: The Stack
Assume:
  ebx=0x00
  esi=0x203040
  edi=0x21F0C0
Inside function
push ebx
push esi
push edi
Address | Value | Instruction
0x1FFCC |  | 
0x1FFD0 |  | 
0x1FFD4 |  | 
0x1FFD8 | c0 f0 21 00 | push edi
0x1FFDC | 40 30 20 00 | push esi
0x1FFE0 | 00 00 00 00 | push ebx
0x1FF20 |  | sub esp, 0xcc
--- | … | 
0x1FFEC | 78 56 34 12 | push ebp
0x1FFF0 | 07 10 40 00 | call calcNewAge
0x1FFF4 | 32 00 00 00 | push age
0x1FFF8 | 0A 00 00 00 | push diff
0x1FFFC | value | 
ESP
EBP=0x0001FFEC

## Slide 21: The Stack – Accessing Args
To access the parameters or local variables by referencing the stack pointer, the program would have to account for every “stack-based” instruction
Address | Value | Instruction
0x1FFCC |  | 
0x1FFD0 |  | 
0x1FFD4 |  | 
0x1FFD8 | c0 f0 21 00 | push edi
0x1FFDC | 40 30 20 00 | push esi
0x1FFE0 | 00 00 00 00 | push ebx
0x1FF20 |  | sub esp, 0xcc
--- | … | 
0x1FFEC | 78 56 34 12 | push ebp
0x1FFF0 | 07 10 40 00 | call calcNewAge
0x1FFF4 | 32 00 00 00 | push age
0x1FFF8 | 0A 00 00 00 | push diff
0x1FFFC | value | 
ESP
EBP=0x0001FFEC

## Slide 22: The Stack – Accessing Args
This is WHY ebp is set to esp and used to reference local variables and function call parameters
mov eax, [ebp+age];
  age is label == 8
  ebp + 8 == 0x1FFF4
  eax=0x00000032
Address | Value | Instruction
0x1FFCC |  | 
0x1FFD0 |  | 
0x1FFD4 |  | 
0x1FFD8 | c0 f0 21 00 | push edi
0x1FFDC | 40 30 20 00 | push esi
0x1FFE0 | 00 00 00 00 | push ebx
0x1FF20 |  | sub esp, 0xcc
--- | … | 
0x1FFEC | 78 56 34 12 | push ebp
0x1FFF0 | 07 10 40 00 | call calcNewAge
0x1FFF4 | 32 00 00 00 | push age
0x1FFF8 | 0A 00 00 00 | push diff
0x1FFFC | value | 
ESP
EBP=0x0001FFEC

## Slide 23: The Stack – Accessing Args
Before function exits, must reset the saved registers
Inside function:
  pop edi
    edi = 0x0021f0c0
  pop esi
    esi = 0x00203040
  pop ebx
    ebx = 0x00000000
Address | Value | Instruction
0x1FFCC |  | 
0x1FFD0 |  | 
0x1FFD4 |  | 
0x1FFD8 | c0 f0 21 00 | pop edi
0x1FFDC | 40 30 20 00 | pop esi
0x1FFE0 | 00 00 00 00 | pop ebx
0x1FF20 |  | sub esp, 0xcc
--- | … | 
0x1FFEC | 78 56 34 12 | push ebp
0x1FFF0 | 07 10 40 00 | call calcNewAge
0x1FFF4 | 32 00 00 00 | push age
0x1FFF8 | 0A 00 00 00 | push diff
0x1FFFC | value | 
ESP
EBP=0x0001FFEC
Note: after “pop” these values remain in stack memory

## Slide 24: The Stack – Accessing Args
Also, must reset the stack pointer and ebp
Inside function:
  mov esp, ebp
    esp = 0x0001FFEC
  pop ebp
    ebp = 0x12345678
    esp = 0x0001FFF0
Address | Value | Instruction
0x1FFCC |  | 
0x1FFD0 |  | 
0x1FFD4 |  | 
0x1FFD8 | c0 f0 21 00 | pop edi
0x1FFDC | 40 30 20 00 | pop esi
0x1FFE0 | 00 00 00 00 | pop ebx
0x1FF20 |  | sub esp, 0xcc
--- | … | 
0x1FFEC | 78 56 34 12 | mov esp, ebp
0x1FFF0 | 07 10 40 00 | pop ebp
0x1FFF4 | 32 00 00 00 | push age
0x1FFF8 | 0A 00 00 00 | push diff
0x1FFFC | value | 
ESP
EBP=0x12345678
Note: after “pop” these values remain in stack memory

## Slide 25: The Stack – Accessing Args
retn
    esp=0x0001FFF4
    eip = 0x00401007
External to the function, where it was called …
  add esp, 8
Address | Value | Instruction
0x1FFCC |  | 
0x1FFD0 |  | 
0x1FFD4 |  | 
0x1FFD8 | c0 f0 21 00 | pop edi
0x1FFDC | 40 30 20 00 | pop esi
0x1FFE0 | 00 00 00 00 | pop ebx
0x1FF20 |  | sub esp, 0xcc
--- | … | 
0x1FFEC | 78 56 34 12 | mov esp, ebp
0x1FFF0 | 07 10 40 00 | pop ebp
0x1FFF4 | 32 00 00 00 | retn
0x1FFF8 | 0A 00 00 00 | push diff
0x1FFFC | value | add esp, 8
ESP
EBP=0x12345678
Note: after “retn” these values remain in stack memory

## Slide 26: Questions & Comments

## Slide 27: References
https://msdn.microsoft.com/en-us/library/windows/desktop/aa365574(v=vs.85).aspx
Intel Reference Manuals
https://en.wikipedia.org/wiki/X86_memory_segmentation