## Slide 1: HARDWARE MATH
Instructor: john ortiz
Lecturer III utsa
stego@satx.rr.com
CS 3843 computer organization

## Slide 2: Logical Operations Review
NOT
  Invert all the bits
  One’s complement
(N) AND
  All inputs must be 1 for result to be one
  Think multiplication: 1 * 1 * 1 * 1 * … if any one of the inputs is a zero, the result is zero
  For NAND, same thing except result is inverted
    If any one of the inputs is a zero, the result is a one

## Slide 3: Logical Operations Review
(N) OR
  If any input is a one, the result is a one
  Think addition, but the result is either zero or not zero
    In order for the final result to be zero, all inputs must be zero
  For NOR, same thing except result is inverted
    In order for the final result to be one, all inputs must be zero
(XOR / XNOR)
  If both inputs are the same, the result is zero
  Think even vs. odd – even number of ones, result is zero
  XNOR is also called “equivalence” because if the inputs are the same , the result is a one

## Slide 4: Logical Operations Review
Bitwise logical operations
  Operates on each bit as specified below
NOT
  ! 0 = 1
  ! 1 = 0
AND OR
  0 & 0 = 0 0 & 0 = 0
  0 & 1 = 0 0 & 1 = 1
  1 & 0 = 0 1 & 0 = 1
  1 & 1 = 1 1 & 1 = 1
XOR
  0 & 0 = 0
  0 & 1 = 1
  1 & 0 = 1
  1 & 1 = 0

## Slide 5: The XOR Gate
An XOR gate can be constructed from basic logical operations such as the two examples below
A | B | OUT
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0

## Slide 6: Hardware Logic
A brief look at the hardware that makes a computer work is based on the logical functions:
  NOT
    inverter
  (N) AND
    Enable / disable - (a one on one input enables the other)
    Mask bits: AND a register with 0x0000000F and all bits except bottom 4 are zero – i.e. masked off
  (N) OR
    Enable / disable - (a zero on one input enables the other)
    Mask bits: OR a register with 0x0000000F to ensure bottom 4 bits are one
  Exclusive-OR (XOR) / Exclusive-NOR (XNOR)
    Controllable inverter – (a one on one input inverts the other, a zero on one input does not)

## Slide 7: Logical – Half Adder
For binary arithmetic, XOR is an adder
  0 + 0 = 0; 0 xor 0 = 0
  0 + 1 = 1; 0 xor 1 = 1
  1 + 0 = 1; 1 xor 0 = 1
  1 + 1 = 2; 1 xor 1 = 0
    Wait! 2 is not equal to zero!
    But there is no “2” in binary, so it is expressed as 10 <one-zero>
    Soooooo, the last digit is a ZERO as in the 1 xor 1
    The 1 in the 2’s place is the carry out of adding 1 + 1
      1 + 1 = zero, carry the one  10
      Just like in decimal arithmetic: 1 + 9 = ten == 0 carry the 1  10
    We can generate a carry in hardware by AND’ing the two inputs
    Only when they are both one is the result a 1
      1 and 1 = 1

## Slide 8: Hardware: Full Adder
The prior circuit was a one-bit half adder because it did not allow for a carry in
Adding a carry in and a little extra circuitry, we construct a one-bit full adder as shown below

## Slide 9: Hardware: 4-Bit Full Adder
For multiple bits, cascade them together in parallel
Shown is a 4-bit full adder
But what about subtraction?
Of course we can build a subtractor
But better is to invert the sign of the
B input (i.e. neg B)
Taking two’s complement requires
inverting all the bits and adding one
XOR is a controllable inverter

## Slide 10: Hardware: Addition & Subtraction
But what about subtraction?
Tie the first carry in to an
“Add/Sub” signal
If that is a ONE, all the bits
will be inverted and
we will add the negative
Initial carry in is the Add One

## Slide 11: Summary of Skills
Logical Operations & Relevant Hardware
i.e. What IS on the test!!!

## Slide 12: Questions & Comments

## Slide 13: References
My brain